## Slide 1
An Introduction to Green Button
Dr. David Wollman Deputy Director, Smart Grid and Cyber-Physical Systems Program Manager, Smart Grid Standards and Research Engineering Laboratory National Institute of Standards and Technology (NIST)
Green Button Download
My Data

## Slide 2: Outline
Introduction
  NIST role, in coordination with OSTP, DOE, FERC, and others
  Smart Grid Interoperability Panel (SGIP)
  Green Button & White House call to action
Green Button Overview
  Recent highlights
  Value story
  Standards foundation and timeline
  SGIP Priority Action Plan support
Green Button Technical Details
  Energy Usage Information standardization
  Green Button file format
  Resources and User Communities

## Slide 3: US Government Roles in Smart Grid
Federal
State
Federal
Energy
Regulatory
Commission
Smart Grid Task Force /
National Science &
Technology Council
Smart Grid
Subcommittee
Other Federal
Agencies (EPA, …)
Office of Science and Technology
Policy; National Economic Council;
Council on Environmental Quality
FERC – NARUC
Smart Response Collaborative
State Public Utility Commissions
Notes: 3

## Slide 4: Standards – Key Aspect of US Smart Grid Policy
The Energy Independence and Security Act of 2007 gives NIST “primary responsibility to coordinate development of a framework that includes protocols and model standards for information management to achieve interoperability of smart grid devices and systems…”
Congress directed that the framework be “flexible, uniform, and technology neutral”
Input to DOE, use of NIST-identified standards as criteria for federal Smart Grid Grants
Input to federal (FERC) and state regulators
The NSTC Subcommittee on Smart Grid Policy: “A Policy Framework for the 21st Century Grid: Enabling Our Secure Energy Future”
OMB/USTR/OSTP January 17, 2012 memo: Principles for Federal Engagement in Standards Activities to Address National Priorities
National Tech Transfer and Advancement Act / OMB A-119 – NIST standards coordination role

## Slide 5: NIST Smart Grid Interoperability Panel
Public-private partnership created in Nov. 2009
Approx. 750 member organizations, 1900+ participants
Open, public process with international participation
Coordinates and accelerates standards development
  Identifies Requirements
  Prioritizes standards development programs
  Works with over 20 SDOs including IEC, ISO, ITU, IEEE, …
Web-based participation
SGIP Twiki:
http://collaborate.nist.gov/twiki-sggrid/bin/view/SmartGrid/SGIP

## Slide 6: What is Green Button? White House call to action
Common-sense idea that electricity customers should be able to download their own energy usage information in consumer- and computer-friendly format.
Notes: 6

## Slide 7: September 2011 – Challenge to Industry January 2012 – Celebrate California launch
As of January 18th, nearly 6 million households and 17 million residents in CA have access to a Green Button.
In conjunction with a recent White House Green Button meeting on March 22, 2012, an additional 9 utilities and many additional vendors committed to implementing and supporting Green Button, increasing the number of households to 27 million that will have Green Button access by the end of 2012.
All 3 CA utilities commit to “green button;” aligns with CPUC rulemaking on privacy, consumer access to energy data, and OIRA “smart disclosure” memo

## Slide 8: What is Green Button data good for?
Source:
Insight: entrepreneur-created web portals analyze energy usage and provide actionable tips;
Heating and Cooling: customized heating and cooling activities for savings and comfort;
Education: community and student energy efficiency competitions;
Retrofits: improved decision-support tools to facilitate energy efficiency retrofits;
Verification: measurement of energy efficiency investments;
Real Estate: provide energy costs for tenants and/or new home purchasers; and
Solar: optimize the size and cost-effectiveness of rooftop solar panels.
Empower Consumers and Spur Innovation
Notes: 8

## Slide 9: What people are saying…
Source:
It may finally give consumers a reason to care about the smart grid.
– SF Chronicle
Solar companies are also eager for consumer data because understanding a homeowner's electricity use is key to the sales process.
– San Jose Mercury News
The project is important because it is a broad-based plan to take energy data and standardize the format of it, open it up (while also providing security) and make it readily available to consumers.
– Gigaom
I'm a big fan of simplicity and open standards to unleash a lot of innovation.…I'm going to reach out to ConEd, the utility in NYC, and find out when they are going to add Green Button support to their consumers data. I hope it is soon.
– Fred Wilson (Venture Capitalist)
Notes: 9

## Slide 10: Green Button Overview
David Wollman, NIST
With acknowledgements to Marty Burns of the EnerNex SGIP administrator team

## Slide 11: What is Green Button?
The vision – collaboration and inspiration, using voluntary adoption of industry standards
From concept to specification to early adopter implementations in 3 months
Green Button Download
My Data

## Slide 12: Green Button Initiative Update
Green Button Rollout in California – January 18th
DOE / Smart Grid Privacy Workshop – January 31st
FERC/NARUC Smart Response Collaborative – February 5th
UCAIug OpenSG OpenADE Task Force Meetings – February
Green Button Workshop – February 29th
DOE Webinar for SGIG Grant Recipients – March 1st
DOE Smart Grid Data Access FOA 579 – March 1st
White House CEO meeting and additional utilities commitments – March 22nd
Today’s Webinar

## Slide 13: GreenButtonData – Live!!
www.greenbuttondata.org
  Developer’s page: http://www.greenbuttondata.org/greendevelop.html

## Slide 14: The Value Story
Why is this of interest to consumers
  Energy Usage Information is feedback mechanism, knowledge is power
… to utilities
  A well established specification will result in low cost of deployment of capabilities already planned and committed.
  A single third party interface encourages value added services that don’t depend on continuous utility innovation on this interface.
… to regulators
  Adoption of demand side management schemes will require consumer feedback and engagement to enable them to benefit. Many regulators are interested in ubiquitous low cost Green Button capabilities to enable consumer engagement and support return on investments.
… to implementers
  A single interface allows robust applications to be developed
  Focus on value added rather than multiple custom interfaces per utility
An ecosystem of goods and services built around concrete standard
  Web applications
  Desktop applications
  Applications within the home: appliances, energy management systems, …

## Slide 15: Consumer Perspective
$
What shall I do?
Here is what I used!
Here is what I’ll plan to use in future
How much did I use?
I now understand what I use and what it cost me.
I know what prices for use will be.
Third party value added services …

## Slide 16: Green Button Enabling Vision
Usage Profile
Overall Usage
Cost of Usage

## Slide 17: Green Button Time Line
OpenADE TF formed
OpenADE Reqs PAP10
NAESB PAP10 Standard Ratified
PAP10 in NIST SGIP CoS
NAESB ESPI Standard Ratified
US CTO Green Button Initiative
CA IOUs Implement
Oracle
Microsoft
Google
Tendril
GreenBox
Control4
EnerNex
Xtensible
SCE
PG&E
Sempra
Oncor
Duke
Reliant
Consumers
Centerpoint
AEP
FPL
ADE Concept Meeting
Many companies pushing Utilities for proprietary 3rd party interfaces
2009
2010
2011
2012
2008
Numerous additional implementations …

## Slide 18: How SGIP Inspired Green Button Format
PAP10 was formed at the start of the SGIP to facilitate the standardization of Energy Usage Information
  Resulted in NAESB (North American Energy Standards Board) REQ18/WEQ19 PAP10 EUI standard in December 2010
  This was an information model standard, a “seed standard”, for other standards to use.
PAP10 EUI was taken up by NAESB REQ21 Energy Services Provider Interface
  Based on UCAIug OpenADE and NAESB PAP10 standards
  Ratified in October 2011
  How to represent EUI in XML, and,
  How to exchange it between utilities and third parties on behalf of consumers
Together these define a flexible file format for Green Button based on ratified standards from NAESB
The initial implementations of Green Button are narrowing in on a specific subset of ESPI and EUI for its realization

## Slide 19: Which is Which
OpenADE: Requirements specification for secure delivery of historical and ongoing usage information to 3rd Party
PAP 10: Seed standard that defines a common energy usage information data model, for use across and interoperability between multiple standards
NAESB ESPI: Standard that satisfies the requirements laid out in OpenADE and incorporates the data model from NAESB PAP 10 Energy Usage Information
Green Button: File format subset of ESPI provides usage information to the consumer’s via Web site

## Slide 20: What Drives Implementation
It was great to get Green Button off the mark with a quick demonstration of its capabilities, it is a bigger goal to support a sustained Green Button-infused ecosystem.
Keys:
  Benefits drive adoption, barriers slow adoption
  Therefore, minimize barriers to adoption
  Three components to drive interoperability: Standards evolution, User Groups/Testing, Reference Implementations
SGIP engagement: Development of new Priority Action Plan (PAP20)

## Slide 21: https://collaborate.nist.gov/twiki-sggrid/bin/view/SmartGrid/GreenButtonESPIEvolution

## Slide 22: SGIP PAP20: Green Button ESPI Evolution
2Q12
3Q12
4Q12
Timeline:
Standards (NAESB)
International Version
T&C (UCAIug)
Implementation (EnergyOS)
REQ18/WEQ19 Maintenance Update
ESPI Errata Update
ESPI New Reqs Update
Green Button Test Plan
ESPI Test Plan
Green Button SDK
OpenESPI
UCAIug ITCA
Specification Deliverables:
SGIP PAP Activities:
Requirements for Green Button and ESPI Rollout
Facilitate / Coordinate SGIP interactions
Privacy assurance recommendations
Cybersecurity recommendations for EUI exchanges
CSWG
Test plan consistency
ITCA assurances
SGTCC
Coordinates with
PAP 20
Where:
Implementation activities not formal part of PAP

## Slide 23: About the deliverables of PAP20 *planned dates to be confirmed at initial PAP20 meetings
SGIP Standing Committee Involvement
  CSWG – Cyber Security and Privacy recommendations for ESPI exchanges
  SGTCC – ITCA formation and test plan development collaboration
NAESB Standards Evolution
  PAP10 Maintenance Update ~4/2012
  ESPI Errata ~4/2012
  ESPI Evolution ~9/2012
UCAIug Test Plans and ITCA (Interoperability Testing/Certification Authority)
  UCAIug ITCA ~6/2012
  Green Button Test Plan ~6/2012
  ESPI Test Plan ~6/2012
Reference Implementations (these activities are not officially part of PAP)
  Green Button SDK evolution ~6/2012
  OpenESPI implementation and Test Harness ~6/2012
International Standardization
  Seek International venue to cross-publish NAESB ESPI standard ~TBD
    ESPI is profile (with extensions) of IEC 61968-9 2nd Edition

## Slide 24: How to Reduce Barriers to Penetration
Standards
Users Groups
Interoperable products and services
Reference Implementations
Implementation agreements
Labeling and Test Certifications
Open Source Running Code
“golden unit”
Consensus among stakeholders
Maintenance and evolution
Issues resolution
Development projects
Activation
Energy
Potential
Energy
Barriers Impede Penetration of New Technology
Benefits Drive Penetration of New Technology
Green Button as Catalyst Speeds Penetration
NAESB
UCAIug
OpenESPI

## Slide 25: Green Button Technical Details
David Wollman, NIST
With acknowledgements to Marty Burns of the EnerNex SGIP administrator team

## Slide 26: What is the constellation of development tools and collaboration environments
Composition of Green Button Data
Green Button SDK
OpenESPI, an open-source ESPI implementation
UCAIug Test Plans

## Slide 27: Composition of Energy Usage Information
UsagePoint
ServiceCategory
MeterReading
IntervalBlock
IntervalReading
ReadingQuality
ReadingType
ElectricPowerSummary
ElectricPowerQuality Summary
Note: This information is multidimensional. Many different reading types, summaries, and readings possible. i.e. not “flat”
EUI comes from and to residences and businesses

## Slide 28: Diversity of information in EUI
Dimensions
Kinds of Data
  Measurements of power, energy, gas, water, …
  Quality: Raw, validated, estimated, …
  Source: Meter near real-time, utility back end, third party
  Economics: Consumers need to know the cost of their consumed power (but we did not construct a pricing model)
  Identification: by customer, device, location
  Readings
  Interval data
  Summary Information
  Power Quality Metrics

## Slide 29: Some examples of Green Button Data
Hourly load profile for past billing period plus current period to date
Fifteen minute load profile for most recent 15 days
Daily load profile for past month or year
Summary only data
Energy usage and energy demand readings
Gas, Water usage profiles
Yearly summary data with monthly parts

## Slide 30: Green Button SDK
GETBatchSampleEUI.xml: Sample Green Button EUI File
ESPIRender_xslt1.xslt: XSLT Rendering Style Sheet
Green Button Data Generator Spreadsheet: Available for download from OpenESPI on GitHub
espi.xsd, atom.xsd: schemas constrain xml documents
NAESB Green Button Portal - http://www.naesb.org/ESPI_Standards.asp
To purchase the NAESB ESPI Standard on which the Green Button file format is based, use the following link: http://www.naesb.org/misc/naesb_matl_order_espi_standards.pdf
http://www.GreenButtonData.org

## Slide 31: Tools that are currently available and how they work
WC3 standard components – xsd, xslt, xml
OpenESPI development environment
Development Virtual Machine
Graphics

## Slide 32: Web Technologies for Definition and Presentation of EUI File Format
X
XML Schema (XSD)
XML
XSLT
Describes the rules of file format
Contains customer EUI data in standard file format and references to XSD and XSLT
Defines how to transform for humans
Standard EUI file Format

## Slide 33: Alternate paths to EUI – single format
Acknowledgements to graphics owners
Single Data Format: all at once
Single Data Format: as sequence
Sources of EUI
Uses of EUI
Via: ESPI, SEP2, Web Portal
Power Utility

## Slide 34: Green Button Schemas: Views in XMLSpy™
“colored text”
“grid view”
“graphic view”

## Slide 35: Green Button Data XML File
IntervalBlock
MeterReading
UsagePoint
ReadingType
IntervalBlock
ElectricPower UsageSummary

## Slide 36: Green Button Schemas: IntervalBlock
IntervalBlock has an Interval time definition
The IntervalReadings have values, cost, and reading quality, as well as optional time period
Note: most parts of schema can be extended

## Slide 37: Green Button Schemas: ElectricPowerUsageSummary

## Slide 38: Green Button Sample XSLT
XSLT
XML
HTML

## Slide 39: Binding Green Button File to XSLT and XSD
Identify XSLT Style Sheet
Identify XSD Schema Location

## Slide 40: Green Button Data File Generator
Set the structure of the intervals and blocks
Set weightings for weekdays and weekends

## Slide 41: OpenESPI Software Architecture
Actors:
  Consumer
  Data Custodian
  EnergyServiceProvider
InformationElements:
  Representations
  EUI Data Repository
UseCases/Sequences:
  Scenario Automatons
  OAuth/AtomPub Patterns
  Orchestration and Deployment
Frameworks:
  Spring Model/View/Controler
  Spring Social (OAuth)
  Apache Wink (AtomPub)
Development Platform:
  Eclipse Projects
  Ubuntu VM
  Java Builds
  C++ Builds (future)
Testing Plans:
  JUnit + Spring Testing Framework
  Selenium Automations

## Slide 42: OpenESPI Frameworks – Spring Profile

## Slide 43: Virtual Machine for OpenESPI Development
The OpenESPI Development Virtual Machine is a Linux Ubuntu desktop environment that may be used to jumpstart your OpenESPI development efforts. Further background on the VM may be found at http://www.openespi.org/vm.html
The VM connects to the GitHub remote repository
All Development Tools, Web Servers, and Test Tools are Incorporated into Free VM
VM Player for Windows is Free
VM Player for Apple is ~$50

## Slide 44: Green Button Graphics*
Green Button Download
My Data
* With permission of Veterans Administration (Blue Button) through “comfort letter”

## Slide 45: Discussion about tools and testing going forward
Where work is occurring
  Acceleration project for testing tools
  User community to support
    A Policy
    A Brand
      What Green Button is
      End user applications
    A Collection of technologies
      Technical standards, test plans and certifications
How to contribute
How to comment/discuss

## Slide 46: How Open Source Can Work With Business Goals
UCAIug
Funders
Funders
Funders
Funders
Consulting / Development Group
OpenESPI / Green Button Apache Licensed Open Source Development Project
OpenADE Task Force
Requirements
SW Development
Funding
Administration
Commercial Products ESPI Implementations
Commercial Products Certification Test Tools
Commercial Products Certifications
Commercial $$ Products and Services
Open Source

## Slide 47: http://collaborate.nist.gov/twiki-sggrid/bin/view/SmartGrid/GreenButtonInitiative

## Slide 48: http://www.naesb.org/ESPI_Standards.asp

## Slide 49: http://osgug.ucaiug.org/sgsystems/OpenADE/default.aspx

## Slide 50: http://openei.org
Green Button Apps

## Slide 51: http://www.openespi.org/

## Slide 52: https://github.com/energyos/OpenESPI

## Slide 53: Issues Resolution
Related to NAESB Standards, Test Plans, Branding of Green Button:
  http://osgug.ucaiug.org/HelpDesk/Lists/servicerequests/GreenButton.aspx
Related to Development Tools, Open Source, Implementation of Test
  https://github.com/energyos/OpenESPI/issues

## Slide 54: Links
NAESB
  NAESB PAP10 Task Force Project Page : http://www.naesb.org/smart_grid_pap10.asp
  NAESB ESPI Task Force Project Page : http://www.naesb.org/espi_task_force.asp
  NAESB ESPI and PAP10 email lists: to subscribe contact Denise Rager at NAESB - drager@naesb.org
  NAESB Green Button Portal - http://www.naesb.org/ESPI_Standards.asp
UCAIug
  UCAIug OpenADE Mail List: http://www.smartgridlistserv.org/cgi/wa.exe?A0=OPENSG-OPENADE
  UCAIug OpenADE Meetings: tuesdays at 3:00 EST - https://www2.gotomeeting.com/join/844935738, 415-363-0070 #844-935-738
  UCAIug OpenADE Green Button Issues List: http://osgug.ucaiug.org/HelpDesk/Lists/servicerequests/GreenButton.aspx
EnergyOS
  EnergyOS OpenESPI Mail List: http://groups.google.com/group/energyos_espi/subscribe?hl=en
  EnergyOS OpenESPI Web Site: http://www.openespi.org/
  EnergyOS OpenESPI Meetings: mondays at 12:00 EST - https://www2.gotomeeting.com/join/129392235, +1 (516) 453-0010 #129-392-235
  EnergyOS OpenESPI GitHub: https://github.com/energyos/OpenESPI
  EnergyOS OpenESPI GitHub Issues List: https://github.com/energyos/OpenESPI/issues
NREL OpenEnergyInfo Green Button Apps Repository: http://en.openei.org/wiki/Main_Page
Green Button Data Web Site: http://www.greenbuttondata.org