## Slide 1: Renewable Energy Project Development and Finance Framework: The 5 Step Process

## Slide 2: Agenda
Strategic Energy Planning
Energy Plan
5 Step Project Development Process

## Slide 3
Strategic energy plannning
Notes: Next I’ll talk in more detail about the project development process.

## Slide 4: What is Strategic Energy Planning?
Brings desired energy future into clear focus
Considers current reality and leverages local resources
Considers hurdles/challenges before you reach them
Maps out efficient path to achieve your desired energy future
Clarifies progress indicators
Documents the game plan for short- and long-term success
And what does it do for you?
vs.
Graphic concepts reprinted with permission from Lesley Kabotie, Kabotie Consulting.
Notes: Success factors – Great Communications – Broad Communications

## Slide 5: What Makes Energy Planning “Strategic”?
Inclusive Energy Planning Process
Public Sector
Tribal/State/Federal
Private Sector
Non-Profit
Stakeholder buy-in to
long-term vision
Political commitment to mobilize authority and resources
Identify energy uses and future needs (baseline)
…
…
Graphic concepts reprinted with permission from Lesley Kabotie, Kabotie Consulting.

## Slide 6: Steps in Strategic Energy Planning
Identify/Convene Stakeholders
Form Leadership Team
Compile Energy Plan
Develop Energy Vision
Assess Energy Needs and Resources
Develop Specific Goals
Prioritize Projects & Programs
Identify Financing Options
Measurement & Verification (M&V) and Plan Alterations

## Slide 7
Energy Plan
Notes: Next I’ll talk in more detail about the project development process.

## Slide 8: Energy Plan: Purpose & Functions
Purpose
Document near-term goals
Sustain momentum
Achieve long-term goals
Functions
Creates “road map” to hold accountability to the destination
Provides the means to consistently share the story with others
Creates resources to help guide and filter priorities, providers, and decisions

## Slide 9: Priorities & Decisions: Develop Specific Goals
Examples:
Reduce electricity use by ___% by 2022
Obtain ___% of electricity from renewable sources within 10 years (similar to a renewable portfolio standard or RPS)
Reduce energy costs by ___% within 5 years
Photo by Brooke Oleen, NCSL

## Slide 10
5 Step Project Development PRocess
Notes: Next I’ll talk in more detail about the project development process.

## Slide 11: Project Development Process: What Is It?
Framework based on experience
Focuses on key decision points
Shows that project development is iterative
Emphasizes that delaying or deciding against a project that does not meet current goals is a viable outcome and option
Notes: Here you’ll see the process we use in these courses to outline the project development process. This process was developed by the DOE Office of Indian Energy and is based on our experience in project development.
There are a number of different frameworks out there, and this is one that we have had experience with being successful in Tribal project development.
We developed this one because it’s based on decision points: what are the decisions that need to be made and by which decision maker (Tribal leader or project manager), and what information is necessary to make those decisions?
We also wanted to illustrate that there are a number of points in the project development process at which you can take an offramp and decide not to pursue the project.
Because this is a process, we’ve added in steps. It is important to understand, though, that the process of developing a project is actually iterative. You invest a little time or money to determine if there is potential, and if there is, you move onto the next step. There you invest a little more money and time to get more detailed information about the project and its impacts. At every point, you have an opportunity to stop the project, with minimal investment. Note that development costs do ramp up once you move on from the early development stage.
That’s an important thing to remember here: if at any stage, you are getting information that indicates that your project is not going to meet your goal, it is a valid decision to decide to delay or rethink. You want to make sure that your goals are clear from the beginning to make sure that you don’t forever put projects on hold.

## Slide 12
1
Potential
3
Refinement
5 Operations & Maintenance
2
Options
4
Implementation
1
Potential
Notes: Slide 12
Here I am showing you the project development and financing strategy. Another way to think of this is as a five-step project development process. It will be used throughout this presentation to highlight where a certain activity or effort falls into the big picture of developing a RE project.
You will notice that this process is depicted as both a circle and as a straight line. This is because when developing a RE project, you may encounter both repetitive processes (as in the circle representation) and sequential processes (as in the line representation). For example, sometimes you may evaluate a project and eventually reach a decision to not proceed on the project any further. At this point you will begin the process anew for another type of development or a variation on the project. On the other hand, there are can be milestones to be met before proceeding to the next phase of development. It is important to have the whole picture in mind not just the step immediately before you, as different processes will proceed at different paces, depending on where your project is located.
Broadly speaking, we have categorized five steps in the process which will be discussed in detail in the remainder of the presentation. These are:
  Project Potential
  Project Options
  Refinement
  Project Implementation
  Operations and Maintenance

## Slide 13: Step 1: Site, Scale, Resource and Market Potential
Purpose: Determine whether basic elements for a successful project are in place
Tasks:
Identify possible sites for project locations
Confirm renewable energy resource
Review Tribal facility electric cost data, regulations, and transmission and interconnection requirements
Evaluate potential markets and paths for renewable sales; identify potential partners/off-takers to sell the project’s power
Assemble or communicate with the right team, those in positions or with knowledge to facilitate, approve, champion the project
Analyze risks: financing, permitting, construction costs
Analyze utility rules: interconnection and transmission
Notes: Slide 13
When determining the potential, the key question to answer is: Is there a viable project?
Analyze what are the risks in the project that could potentially kill the project (so called high level fatal flaw review)
  Examples: securing the site, confirming the energy resource, estimating the project economics, determining the markets and potential pathways, and assembling the right team or the human capital
For example: you want to look for an appropriate site for the project. You may have several potential sites, but also have some areas that are really off limits for development of this kind of project. It’s important to know where the boundaries are. As part of our curriculum, the DOE Office of Indian Energy has developed a series of on-demand courses on foundational renewable energy topics that you can watch at any time. One of these course goes over “Assessing Energy Resources,” which would be helpful during this step of the process because it provides information on tools you can use to identify potential project sites.
Part of the process for determining if there is a viable project is to determine a few main points:
To whom can you sell electricity?
How much will that entity pay for electricity?

## Slide 14: The Electricity Grid (Overview)
Notes: Electric power systems are real-time energy delivery systems. Real-time means that power is generated, transported, and supplied the moment you turn on a switch. Generators must produce energy as a consumer calls for it. Two representations of the electricity grid are shown on this slide. Both figures show the basic building blocks of the electricity grid. The diagram on the top shows the basic system components while the one on the bottom shows an electrical schematic diagram of the same system. The production of electrical energy starts with generation. A generating station transforms other sources of energy into electrical energy. The electrical energy is then transformed at a transmission substation before being transported long distances over high voltage transmission lines. As I will detail later in this presentation, high voltage power lines are needed to efficiently transport the energy over long distances between the generation source and the industrial, commercial, and residential customers. Distribution substations transform the high-voltage energy into lower-voltage energy that is more suitable for delivery to its final destinations.

## Slide 15: Electricity Transmission System
Source: http://www.osha.gov/SLTC/etools/electric_power/illustrated_glossary/transmission_lines.html
345 kV
230 kV
Transmission
Voltage Levels
Transmission
230 kilovolt (kV)
345 kV
500 kV
765 kV
1,000 kV and above
Sub-transmission
69 kV
115 kV
138 kV
69 kV
Notes: The vast interconnection of high voltage transmission lines across the United States is pictured.
The table on the right side of the slide shows the typical transmission and subtransmission voltages used.
Subtransmission voltages are used to transport energy over medium distances (i.e., across large populated areas).
Why do we use high-voltage transmission lines?
High-Voltage transmission lines transport power over long distances efficiently.
High voltage transmission takes advantage of the power equation: (Power = Voltage x Current).
If the voltage is high then the electrical current is reduced so smaller wires can be used.
The losses associated with the transportation of electrical energy are a function of the square of the current flowing in the conductors. In other words, we should strive to transmit power at the highest practical voltage to minimize losses
Various tower structures pictured. Lattice, wood, and tubular steel.
Transmission lines are supported by insulators to prevent flashover to the towers. Notice that as the voltage level goes up the number of insulators in the string increases too.

## Slide 16
1
Potential
3
Refinement
5 Operations & Maintenance
2
Design
4
Implementation
2
Options
Notes: Slide 16
Now lets move on to step 2 in the process: project options!

## Slide 17: Step 2: Project Ownership and Regulatory Options
Purpose: Determine ownership structure and determine permitting considerations
Tasks:
Identify final resource and project location
Understand ownership structure/Tribal role and risk allocations
Narrow financing options
  Clarify tax-equity structure
Initiate EPC procurement process
Understand and plan for permitting, interconnection (and transmission)
Resources:
DOE Office of Indian Energy renewable energy technology-specific webinars:
http://www.energy.gov/indianenergy/resources/education-and-training.
Notes: Slide 17
To narrow your project options, you need to:
  Identify final resource and project location
  Understand ownership structures/Tribal role and risk allocations
  Narrow financing options
    Clarify tax-equity involvement (which is very likely for commercial scale)
  Initiate EPC procurement process
  Understand and plan for permitting, interconnection (and transmission)
The advanced courses have more detail on each of these tasks. In the next few slides, I’ll get into a few of the most critical concepts that you need to understand at a high level.
The idea is to come out of each step being able to make the decision that the project is one that you can continue to develop. Up to this point, you’ve invested a lot of time and a little money. In the next steps you’ll probably be investing a lot more money, and it’s important at the end of this step to take stock of whether or not the project is viable and meets your Tribes goals of developing the project.

## Slide 18
1
Potential
3
Refinement
5 Operations & Maintenance
2
Options
4
Implementation
3
Refinement
Notes: Slide 18
Here we move to step 3 in the process: project refinement

## Slide 19: Step 3: Project Refinement
Purpose: Validate decisions and finalize project structure
Tasks:
Finalize ownership structure and project team identification
Finalize permitting (including environmental reviews), interconnection
Finalize technology, financing, and development costs
Outputs:
Proposed financing/commitments and organization structure
Detailed economic models
Vendors selected
Completed environmental reviews and finalized permits
Off-take and interconnection agreement
Transmission finalized, if necessary
Notes: Slide 19
In this step, there are a lot of decisions to be made by the Tribal leaders. For example:
    Who will be the project developer? And how will you select them? This is done through a procurement process, and we talk more about this in our advanced series of courses. Also, the DOE Office of Indian Energy resource library contains links to useful documents that can assist in the design and roll out of these procurement efforts, so that you are most likely to get a good deal.
    Are the permits in motion? This can also be the job of the developer (if it isn’t the Tribe), and will most likely require hiring professionals knowledgeable in state, local and Tribal laws.
    What are the real, brass tacks costs and financing options for this project (that’s developed by the staff), and which one will you go with (determined by the leadership)?

## Slide 20
1
Potential
3
Refinement
5 Operations & Maintenance
2
Options
4
Implementation
4
Implementation
Notes: Slide 20
We are now turning to the 4th step in the process, the implementation phase.

## Slide 21: Step 4: Implementation
Purpose: Contract for, realize physical construction of project
Tasks:
Finalize project agreements
Finalize vendor contracting process
Finalize preconstruction tasks
Realize construction and equipment installation
Realize interconnection
Realize project commissioning leading to commercial operations
Output: Completed project (commercial operation)
Notes: Slide 21
In this step, which can be among the longer of the steps, you finalize all the partnerships and technology agreements, complete the interconnection with the utility, and get all the financing in order and executed so you can build the project.
When the project implementation is done, which is often done by the developer, the renewable power project is commissioned and operation begins.

## Slide 22: Project Development Process
1
Potential
3
Refinement
5 Operations & Maintenance
2
Options
4
Implementation
5 Operations & Maintenance
Notes: Slide 22
Now lets turn to the long term care of the project: the operations and maintenance functions.
Overall, this step is the longest of them all because it spans the entire life of the project.

## Slide 23: Step 5: Operations & Maintenance
Photo from Florida Solar Energy Center, NREL 14728
Purpose: Conduct or ensure ongoing O&M, including repair and replacement (R&R)*
O&M Costs:
Equipment maintenance and upkeep
Gearbox/inverter replacement
Insurance
Labor and staffing
Extended warranty agreements
If leasing, lessor often manages maintenance
If PPA, vendor typically manages maintenance
* Esp. if owner – role of highest O&M risk
Notes: Slide 23
Operations and maintenance, also called O&M, is the long term care of the renewable energy project to ensure maximum operating efficiency and availability.
Depending on the role selected by the Tribe, the renewable energy asset may be managed by a qualified 3rd party or the Tribe itself.
O&M costs for renewable power plants tends to be much less than fossil plants because there typically is no fuel cost (the exception is biomass). However, there are other maintenance costs to consider, including:
Equipment maintenance and upkeep (including using water to clean PV panels)
Gearbox replacement (Wind turbine); or inverter replacement for solar
Insurance
Labor and staffing
Extended warranty agreements
The developer partner will often have this in their proposal, if you have a partner.

## Slide 24: Not Quite Done!
Check back in with planning document – update as necessary
Identify next potential project from plan
Notes: Now that the facility is operating and being maintained, you may think that’s it’s a done deal, but it’s not!
It’s now a part of your energy and financial portfolio. Integrating this project into your energy planning process is critical to making sure that what you learned from this project is carried into future projects.
From there, you can follow this same cycle as you approach additional potential projects that you’ve identified in your comprehensive energy plan.

## Slide 25: Summary of Actions by Step
1
Potential
3
Refinement
5 Operations & Maintenance
Data Collection and Opportunity Assessment
Options and Strategies
Planning and Development
Financing and Construction
2
Options
4
Implementation
Step 1: Gather all relevant data in order to make first pass at potential project; understand Tribal role options
Step 2: Estimate value to Tribe; begin to identify offtakers, partners, vendors
Step 3: Finalize economic assumptions and roles, interconnection and offtake agreements, partnerships, ownership structure
Step 4: Financial close and construction, vendor contracting completion, project commercially delivered
Step 5: Maintenance plan implementation
Celebrate!
Notes: This has been a VERY high level overview of this project development framework. It’s very important to remember that this process is iterative and involves increasing refinement of information in order to know if the project is going to achieve the Tribe’s goals.